## Slide 1: Inter-Device Media Synchronization in Multi-Screen Environment
Geun-Hyung Kim, Dong-Eui University
Sunghan Kim,
Electronic and Telecommunications Research Institute

## Slide 2: Contents
Introduction
  media synchronization and multi-screen environment
multi-screen service migration
use cases in multi-screen service migration
overall architecture
issues and conclusion

## Slide 3: Introduction (media synchronization)
media synchronization
  important issue to guarantee the QoE (Quality of Experience) of any media session in convergence service
  inter-media synchronization on a single device has been investigated intensively
    media (or contents) delivered along a single delivery path
      e.g., (digital) broadcasting, OTT
    media (or contents) delivered along different delivery paths
      e.g., hybrid broadcast or hybridcasting
  inter-media synchronization on several devices is discussing lately.

## Slide 4: Introduction (multi-screen environment)
users own multiple devices
  that have a connection to the Internet.
  that are connected each other
  that have different computational capacity and different screen size
examples of web-based convergence services
  public (broadcasting content etc.) + personal services (internet poll, supplement information, personal advertisement etc.)

## Slide 5: Service migration
basic example of seamless service migration
watching a movie through smart TV
at home
keep watching the movie with his
smart phone on the way to the campus
watching the movie with notebook to
utilize bigger screen that smart phone

## Slide 6: Multi-Screen Service Migration

## Slide 7: Multi-Screen Service Migration
Device shift
  simple service (content) migration pattern
  whole content will be migrated from one screen to other screens seamlessly
  users can enjoy the same content on their various devices
  service session information should be synchronized to continue service experience seamlessly
Cooperative screen
  partial service (component or content) will be migrated to other screen
  content migration to overcome the limitation of a single screen size (virtual screen)
  multiple screens interact each other to provide rich service experience after migration occurs
  e.g., game control and display area (or component) expansion
Screen Sharing
  partial service (supplemental information) will be migrated to other screen
  an example of supplemental information: the information about actor, actress, or player

## Slide 8: requirements
Synchronized media presentation on each individual screen in the multi-screen environment
  it is necessary to have a coherent orchestration of multiple devices’ content presentation experience
Synchronously seamless migration of whole content (or partial content) that runs on one screen (browser) initially to other screen (browser)
Synchronously seamless replication of whole content that runs on one screen (browser) initially to other screen (browser)
synchronously seamless migration of partial content that runs on one screen (browser) initially to other screen (browser)
Synchronization between TV content and web-based supplemental contents. that can be migrated to other screen

## Slide 9: example of service migration procedure
1
2
3
4
5

## Slide 10: example of service migration
web content sharing

## Slide 11: Simple Architecture
inter-device media synchronization
  exchanging playback timing information periodically between devices via IP networks

## Slide 12: issues
direct or indirectly network device discovery (cross-browser)
direct communication or indirect communication for exchanging timing information (cross-browser)
signaling information to migrate service component seamlessly
component-based web application authoring mechanism to migrate specific component to other screen

## Slide 13: Conclusion
investigate the multi-screen service migration pattern
investigate the issues on inter-device media synchronization and seamless service migration in multi-screen environment

## Slide 14
Thanks for your listening.