## Slide 1: Orchestrate Web of Things by Node-RED and Node Generator
Hitachi, Ltd.
Research and Development Group
Kunihiko Toumura

## Slide 2: 1. Web of Things and Thing Description
IoT
Platform A
IoT
Platform B
IoT
Platform C
IoT
Platform D
Cross-platform
IoT Application
WoT Thing Description describes each IoT Platform and Things,
and Applications use the TD as an open specification of each PF or Things.
WoT Thing Description
Public Security Configuration
Interaction Affordances
General Metadata
Data Schemas
Protocol Binding(s)

## Slide 3: 2. Node-RED: the Well-known Low-code Development Tool
Node-RED is a flow-based programming environment for IoT application.
Developing application is simple: place and connect the “nodes”.
Node-RED is widely used in IoT application development field,
because of its intuitive programming user interface.

## Slide 4: 3. Combine Node-RED with the Web of Things
“Node Generator” simplifies IoT application development
by generating Node module of Node-RED from a Thing Description
WoT Thing Description
Public Security Configuration
Interaction Affordances
General Metadata
Data Schemas
Protocol Binding(s)
Node
Generator
By generating a Node, developer can handle a Node as an avatar of a Thing.
  To write a property of the Thing, send message and its payload will be written.
  To read a property, send a message as a trigger, and then the Node emit a message which contains a value of the property.

## Slide 5: 4. How to Use: Generate and Install a Node Module
0. Install Node Generator
% npm install –g node-red-nodegen
1. Generate a Node module
% node-red-nodegen td.jsonld
2. Install to Node-RED
% cd ~/.node-red
% npm install
generated-module-dir
3. Run Node-RED
% node-red

## Slide 6: 5. How to Use: Write a Simple Application

## Slide 7: 6. How to Use: Control the Thing using Dashboard

## Slide 8: 7. Resources
W3C Web of Things
  Working Group Page: https://www.w3.org/WoT/WG/
  Architecture: https://www.w3.org/TR/wot-architecture/
  Thing Desciption: https://www.w3.org/TR/wot-thing-description/
Node-RED: https://nodered.org/
Node generator:
  Document: https://github.com/node-red/node-red-nodegen/blob/master/docs/index.md
  GitHub: https://github.com/node-red/node-red-nodegen
  Npm: https://www.npmjs.com/package/node-red-nodegen